Section 00000

Security Access and Surveillance

HONEYWELL VIDEO SYSTEMS GENERAL PURPOSE HIGH RESOLUTION DSP COLOR VANDAL MINI FIXED DOME CAMERA

PART 1 – GENERAL

The intent of this document is to specify the minimum criteria for the design, supply, installation, and commissioning of the High Resolution DSP Color Vandal mini fixed dome camera.

  - SUMMARY

- The general purpose High Resolution DSP Color Vandal mini fixed dome camera shall have a low light sensitivity of 0.6 lux @ f1.3 and a minimum 540 TV lines of resolution. The camera shall have a build in 3.6x Vari-focal auto iris lens, with a focal length of 2.8 – 10mm. The indoor/outdoor Vandal fixed mini dome system shall provide multiple methods of installation including: surface mounting onto ceiling or wall, recessed mounting in ceiling or wall as well as to a standard 4S deep electrical box. An adapter plate is also provided for additional support when mounting to ceiling tiles or drywall

  - REFERENCES

- Conformity for Europe (CE)

- Federal Communications Commission (FCC)

- National Television System Committee (NTSC)

- Phase Alternation Line (PAL)

  - DEFINITIONS

- No Substitutes:  The exact make and model number identified in this specification shall be provided without exception.

- Or Equal:  Any item may be substituted for the specified item provided that in every technical sense, the substituted item provides the same or better capability and functionality.

- Or Approved Equal:  A substitute for the specified item may be offered for approval by the Owner.  The proposed substitution must, in every technical sense, provide the same or better capability and functionality as the specified item.  Such requests for approval shall be submitted in accordance with the provisions of PART 1.05 – SUBMITTALS, and must be obtained within the time frames outlined.

  - SYSTEM DESCRIPTION

- The general purpose, High Resolution DSP Color Vandal mini fixed dome camera shall have a low light sensitivity of 0.60 lux @ f1.3 and a minimum 540 TV lines of resolution.  The camera shall be designed for a broad range of surveillance applications and feature Digital Signal Processing (DSP) for clean, sharp images.

  - SUBMITTALS

- General:  Submittals shall be made in accordance with the Conditions of the Contract and Submittal Procedures Section.

- Shop Drawings and Schematics:  Shall depict the High Resolution DSP Color Vandal mini fixed dome camera in final proposed “as built” configuration.  The following must be provided:

- Connection diagrams for interfacing equipment.

- List of connected equipment.

- Locations for all major equipment components to be installed under this specification.

- Product Data:  The following shall be provided:

- Technical data sheets.

- A complete set of instruction manuals.

- Quality Assurance Submittals:  The following shall be submitted:

- Checkout Report:  The Contractor shall provide the Owner with a checkout report for each High Resolution DSP Color Vandal mini fixed dome camera.  The report shall include:

- A complete list of every device.

- The date it was tested, and by whom.

- If retested, the date it was retested, and by whom.

- The final test report shall indicate that every device was tested successfully.

- Manufacturer’s Instructions:  The Contractor shall deliver TBD sets of System Operation and Maintenance Manuals (if available) to the Owner.

- Notice of Completion:  When the final acceptance has been satisfactorily completed, the Owner shall issue a notice of completion to the Contractor.

  - QUALITY ASSURANCE

- Manufacturer’s Qualifications:  The High Resolution DSP Color Vandal mini fixed dome camera manufacturer shall be the world’s largest and most experienced manufacturer of electronic security systems, with over seventy years of experience in the security industry.  The manufacturer shall provide 24/7 technical assistance and support via a toll-free telephone number at no extra charge.

  - DELIVERY, STORAGE, AND HANDLING

- General:  Delivery, storage, and handling of the High Resolution DSP Color Vandal mini fixed dome camera shall be in accordance with the manufacturer’s recommendations.

- Ordering:  The manufacturer’s ordering instructions and lead-time requirements must be followed in order to avoid installation delays.

- Delivery:  The High Resolution DSP Color Vandal mini fixed dome camera shall be delivered in the manufacturer’s original, unopened, undamaged container with identification labels intact.

- Storage and Protection:  The High Resolution DSP Color Vandal mini fixed dome camera shall be stored and protected from exposure to harmful weather conditions and at the environmental conditions recommended by the manufacturer.

  - PROJECT CONDITIONS

  - SEQUENCING

  - SCHEDULING

  - WARRANTY

- General:  The warranty period shall be a minimum of thirty-six (36) months from the manufacture date code under normal use and service.

  - MAINTENANCE

- Preventative Maintenance Agreement During Warranty: As a separate price item, the Contractor shall provide preventative maintenance during the warranty period.  Maintenance shall include, but no be limited to:

- Labor and materials, at no additional cost, to repair the High Resolution DSP Color Vandal mini fixed dome camera.

- Labor and materials, at no additional cost, to provide test and adjustments to the High Resolution DSP Color Vandal mini fixed dome camera.

- Regular inspections.

- Preventative Maintenance Agreement:  As a separate price item, the Contractor shall provide a complete Maintenance Agreement for a period of TBD months after the conclusion of the warranty period.  The Maintenance Agreement shall include, but not be limited to:

- Labor and materials, at no additional cost, to repair the High Resolution DSP Color Vandal mini fixed dome camera.

- Labor and materials, at no additional cost, to provide test and adjustments to the High Resolution DSP Color Vandal mini fixed dome camera.

- Regular inspections.

  - TRAINING

- Operator training shall be conducted for a minimum of TBD sessions, with a minimum session length of TBD hours at the customer’s site.

- Training shall include, but not be limited to, the High Resolution DSP Color Vandal mini fixed dome camera operation and diagnostics.

PART 2 – PRODUCTS

2.01	MANUFACTURED UNITS

- Model Number/Description Table

| HD4CH | 1/3” CCD, 540 TVL DSP Color Vandal Mini Fixed Dome camera, 2.8 – 10mm VFAI lens, Surface or Flush housing, 12VDC/24VAC, NTSC |
| --- | --- |
| HD4CHX | 1/3” CCD, 540 TVL DSP Color Vandal Mini Fixed Dome camera, 2.8 – 10mm VFAI lens, Surface or Flush housing, 12VDC/24VAC, PAL |

  - SYSTEM PERFORMANCE

- The High Resolution DSP Color Vandal mini fixed dome camera shall include, as a minimum, the following features/functions/specifications:

- The High Resolution DSP Color Vandal mini fixed dome camera must be protected by the most extensive support services in the industry, including Customer Service, Pre-Sales Applications Assistance, After-Sales Technical Assistance, access to Technical Online Support, and Online Training using web conferencing.

- The High Resolution DSP Color Vandal mini fixed dome camera and its components shall be thoroughly tested before shipping from the manufacturer’s facility.

- The High Resolution DSP Color Vandal mini fixed dome camera shall incorporate a 1/3-inch digital signal processing (DSP), and a minimum of 540 TV lines of resolution utilizing an effective pixel count of no less than 768 (H) x 494 (V) NTSC, 752 (H) x 582 (V) PAL.

- The High Resolution DSP Color Vandal mini fixed dome camera shall provide excellent color performance in extremely low light, down to 0.6 lux @ f1.3 (50IRE).

- The High Resolution DSP Color Vandal mini fixed dome camera shall have an internal amplifier that applies gain to the signal from the DPS video imaging system.  The amplifier must operate when there is insufficient light in the scene to produce an acceptable video output level, and must only apply as much gain as is necessary.  The camera shall incorporate one level of automatic gain compensation (AGC),  allowing the user to achieve the optimal balance of noise and low light performance in demanding environments.

- The High Resolution DSP Color Vandal mini fixed dome camera shall support the use of Auto Iris/Direct Drive lens connected to the camera via 4-pin molex socket located from the front of the camera board.  The camera must provide DC power drive signal to the lens. The camera must provide power to the lens.Iris level controls are potentiometers accessible from the front of the camera

- The High Resolution DSP Color Vandal mini fixed dome camera shall include a switching 12VDC/24VAC power supply.  The camera must have the ability to synchronize the video output to the AC power input so that all cameras on the system may be synchronized to the same point on the AC supply.  In order to sync cameras on different phases, a phase adjustment control shall be provided through a One Push Button accessible from the front of the camera. The phase shall be adjustable from 0 to 360 degrees. The camera must also include internal synchronization capabilities.

- The power consumption of the High Resolution DSP Color Vandal mini fixed dome camera shall be no more than 4.0 watts.

- The High Resolution DSP Color Vandal mini fixed dome camera shall have a signal to noise ratio of 50 dB with the AGC off.

- The High Resolution DSP Color Vandal mini fixed dome camera shall incorporate auto-tracking white balance to constantly monitor the light and adjust its color. The automatic white balance ranges shall be selectable using a DIP (dual in line package) switch from the front of the camera. The ATW setting shall be the default setting and have a color temperature range of 2800 to 7500 K. The ATW-Wide setting shall have a color temperature range of 2800 to 11000 K.

- To allow the image to be viewed properly on a standard monitor, the High Resolution DSP Color Vandal mini fixed dome camera’s default gamma value must be 0.45.

- The High Resolution DSP Color Vandal mini fixed dome camera shall be the Honeywell Video Systems HD4CH (NTSC) or HD4CHX (PAL) or equivalent.

  - MECHANICAL SPECIFICATIONS

- The High Resolution DSP Color Vandal mini fixed dome camera must have the following mechanical specifications:

- Unit Dimensions (HxD)	3.6” x  5.5”

(91.5mm x 140.6mm)

- Unit Weight	2.5 lb. (1.1 kg)

- Video Output	Composite Video (75ohms)

- Auto Iris Output	4-pin molex

- Color	Light Gray Powder Coating

  - ELECTRICAL POWER REQUIREMENTS

- The High Resolution DSP Color Vandal mini fixed dome camera must have the following electrical specifications:

1.  Voltage	12VDC/24VAC

2.  Power Consumption	<3.5 watts max

  - ENVIRONMENTAL CONDITIONS

- The High Resolution DSP Color Vandal mini fixed dome camera shall be designed to meet the following environmental conditions:

- Operating Temperature	14° to 122° F (-10° to 50° C)

- Storage Temperature	-49° to 167° F (-45° to 75° C)

- Emissions	FCC:  Part 15, Class A

CE:  EN55013

- Immunity	CE (EN50130-4)

- Safety	EU: 73/23/EEC LVD, UL60065

PART 3 – EXECUTION

3.01  EXAMINATION

- Submission of a proposal confirms that the contract documents and site conditions are accepted without qualifications unless exceptions are specifically noted.

- The site shall be visited on a regular basis to appraise ongoing progress of other trades and contractors, make allowances for all ongoing work, and coordinate the requirements of this contract in a timely manner.

- The High Resolution DSP Color Vandal mini fixed dome camera must be inspected before installation, and shall be free of any cosmetic defects or damage.

3.02  PREPARATION

- Prior to installation, the High Resolution DSP Color Vandal mini fixed dome camera shall be configured and tested in accordance with the manufacturer’s instructions.

3.03  INSTALLATION

- The High Resolution DSP Color Vandal mini fixed dome camera must be installed, programmed, and tested in accordance with the manufacturer’s instructions.

- In order to ensure a complete, High Resolution DSP Color Vandal mini fixed dome camera, for bidding purposes, where information is not available from the Owner upon request, the worst-case condition shall be assumed.

- Interfaces shall be coordinated with the Owner’s representative, where appropriate.

- All necessary backboxes, racks, connectors, supports, conduit, cable, and wire must be furnished and installed to provide a complete and reliable High Resolution DSP Color Vandal mini fixed dome camera installation.  Exact location of all boxes, conduit, and wiring runs shall be presented to the Owner for approval in advance of any installation.

- All conduit, cable, and wire shall be installed parallel and square with building lines, including raised floor areas.  Conduit fill shall not exceed forty percent (40%).  All wires shall be gathered and tied up to create an orderly installation.

3.04  TESTING AND CERTIFICATION

- The Contractor shall demonstrate the functionality of the High Resolution DSP Color Vandal mini fixed dome camera upon completion of installation, documenting the result of all tests and providing these results to the Owner.  The High Resolution DSP Color Vandal mini fixed dome camera shall be tested in accordance with the following:

- The Contractor shall conduct a complete inspection and test of all installed High Resolution DSP Color Vandal mini fixed dome camera equipment.  This includes testing and verifying operation with connected equipment.

- The Contractor shall provide staff to test all devices and all operational features of the system for witness by the Owner’s representative and the Authority Having jurisdiction.  All testing must be witnessed by the Owner’s representative, prior to acceptance.

- The testing and certification shall take place as follows:

- The High Resolution DSP Color Vandal mini fixed dome camera shall be tested in conjunction with the manufacturer’s representative.

- All deficiencies noted in the above test shall be corrected.

- Test results shall be submitted to the consultant or Owner’s representative.

- The test and correction of any deficiencies shall be witnessed by the owner’s representative, and note.

- The Owner’s representative shall accept the system.

- The system test shall be witnessed by the Authority Having Jurisdiction.  Any deficiencies noted during the testing must be corrected.

- A letter of certification shall be provided to indicate that the tests have been performed, and all devices are operational.

END OF SECTION

Brief Specification

The High Resolution DSP Color Vandal mini fixed dome camera shall incorporate a 1/3-inch digital signal processing (DSP), and a minimum of 540 TV lines of resolution.  The High Resolution DSP Color Vandal mini fixed dome camera shall provide excellent color performance in extremely low light, down to 0.60 lux @ F1.3 (50IRE).  The High Resolution DSP Color Vandal mini fixed dome camera shall have an internal amplifier that applies gain to the signal from the DPS video imaging system.  The amplifier must operate when there is insufficient light in the scene to produce an acceptable video output level, and must only apply as much gain as is necessary.  The camera shall incorporate a variable automatic gain compensation (AGC), allowing the user to achieve the optimal balance of noise and low light performance in demanding environments.  The High Resolution DSP Color Vandal mini fixed dome camera shall support the use of Auto Iris/Direct Drive lens connected to the camera via a 4-pin socket located on the  front of the camera and must provide power to the lens.  The High Resolution DSP Color Vandal mini fixed dome camera shall include a switching 12VDC/24VAC power supply.  The camera must have the ability to synchronize the video output to the AC power input so that all cameras on the system may be synchronized to the same point on the AC supply.  In order to sync cameras on different phases, a phase adjustment control shall be provided.  The camera must also include internal synchronization capabilities.  The power consumption of the High Resolution DSP Color Vandal mini fixed dome camera shall be no more than 4.0 watts.  The High Resolution DSP Color Vandal mini fixed dome camera shall have a signal to noise ratio of 50 dB with the AGC off.  The High Resolution DSP Color Vandal mini fixed dome camera shall incorporate auto-tracking white balance to constantly monitor the light and adjust its color.  To allow the image to be viewed properly on a standard monitor, the High Resolution DSP Color Vandal mini fixed dome camera’s default gamma value must be 0.45. The indoor/outdoor vandal fixed mini dome system shall provide multiple methods of installation including: surface mounting onto ceiling or wall, recessed mounting in ceiling or wall as well as to a standard 4S deep electrical box. An adapter plate is also provided for additional support when mounting to ceiling tiles or drywall. The High Resolution DSP Color Vandal mini fixed dome camera shall be the Honeywell Video Systems HD4HR (NTSC), HD4CHX (PAL) or equivalent.